## Slide 1: Harmonia: Near-Linear Scalability for Replicated Storage with In-Network Conflict Detection
Hang Zhu
Zhihao Bai, Jialin Li, Ellis Michael
Dan R. K. Ports, Ion Stoica, Xin Jin
Notes: I will present our work
This is a joint work with people at Johns Hopkins University, university of washington, microsoft rearch and UC berkeley

## Slide 2: Replication: fundamental tool for distributed storage
clients
replication protocol to ensure consistency
request
reply
…
Best case: the performance of a single node
Notes: Failures are a regular appearance in large-scale distributed systems, and replication can mask these failures.
One might hope adding more servers to increase not just the reliability but also the system performance
However, some replication protocol has to run to ensure consistency.
And the best case is to achieve only the performance of a single node, such as chain replication, nopaxos

## Slide 3: Achieve linear scalability with strong consistency?
Naïve approach: allow any replica to serve read
  Read-ahead anomalies
    Primary-backup protocols
  Read-behind anomalies
    Quorum-based protocols
Protocol-level approach: CRAQ
  An extra phase for each write
  Unclear how to extend to other protocols
Notes: one naive approach is ...
However, writes cannot be applied instantly across all the replicas, so naively doing so will violate consistency.
We categorize the resulting anomalies into two kinds.
Read-ahead anomalies: which means uncommitted data may be returned. it usually happens for primary-backup protocols
Such as primary-backup, chain replication
Read-behind anomalies: which means stale data may be returned. it usually happens for quorum-based protocols
Such as Viewstamped Replication, NOPaxos,…
But CRAQ adds an

## Slide 4: Our Approach: Harmonia
Design goals
  Generality
    support different protocols
  Minimal overhead
    avoid additional overhead of tracking the dirty set (objects with pending writes)
    In-switch implementation
Key observation: the size of dirty set at any given time is small
Basic idea
  Send reads without pending writes to any replica
  Pass other requests to the underlying replication protocol
Notes: Our approach harmonia is designed for generality
Avoid additional overhead of tracking the dirty set which contains the objects with pending writes
such goal is realized by its in-switch implementation
Key observation: making it possible to track the dirty set on the limited switch memory

## Slide 5: Harmonia Architecture
dirty set
obj_id | seq
E | 1
… | …
sequence number
last-committed point
Clients
Read-Write
Conflict Detection
Storage Servers
Replicated Storage Rack
L2/L3 Routing
ToR Switch Data plane
Notes: Here we show harmonia architecture in one typical deployment scenario where it is placed on the ToR switch of a dedicated storage rack. Besides the Layer2/Layer3 routing, we have the RW conflict detection
which consists of three components.
The dirty set stores the objId and the seqnumber
seq number and last-committed point are used for guaranting consistency

## Slide 6: How to build a strongly consistent replicated system with near-linear scalability?
How to maintain the dirty set in network?
How to achieve near-linear scalability?
How to guarantee consistency?
How to handle failures?
Notes: Basically, Harmonia answers the question: how to build.

## Slide 7: How to build a strongly consistent replicated system with near-linear scalability?
How to maintain the dirty set in network?
How to achieve near-linear scalability?
How to guarantee consistency?
How to handle failures?
Notes: At first, let's see how harmonia maintains the dirty set in network

## Slide 8: Programmable switch architecture
Custom
parser
packets
Ingress pipeline
match
action
Stage 1
Stage 2
…
Queues
Egress pipeline
Stage 1
…
…
…
Register array
Register array
Register array
Notes: Now let’s get a basic idea of the programmable switch arch.
The packets will go through a custom parser and enter the ingress pipeline
There are multiple stages in the pipeline
each stage contains several MA table and also a register array that can be accessed at line rate
Then the packets enter the queues and the egresss pipeline and at last,
are sent out.

## Slide 9: Harmonia packet format
ETH
IP
TCP/UDP
TYPE
SEQ_NUM
Payload
Existing Protocols
Harmonia Header
READ, WRITE, etc.
reserved
port #
L2/L3 Routing
OBJ_ID
Notes: Then we show the custom packet header for Harmonia.
We have a reserved Layer 4 port for harmonia packets.
Harmonia header is at the begininng of the Layer 4 payload, including...

## Slide 10: Insert into dirty set
obj | seq
E | 1
B | 2
obj | seq
X | 3
C | 4
obj | seq
A | 6
Q | 5
h1(A)
h2(A)
Write Query (obj_id=A)
h3(A)
Stage 1
Stage 2
Stage 3
Index the register arrays with the hash of object ID
Iterate over stages until find an empty slot
Store the object ID and the sequence number
Notes: we use the multi-stage register arrays to store the dirty set.
In this figure, we show when it comes a write query with objid A. We use the hash of the objid as the index of the register array
And the switch will go through multiple stages with different hash functions until it finds a empty slot and stores…

## Slide 11: Remove from dirty set
obj | seq
E | 7
B | 8
obj | seq
X | 9
C | 10
obj | seq
Q | 11
h1(A)
h2(A)
Write Completion (obj_id=A, seq=6)
Stage 1
Stage 2
Stage 3
h3(A)
Iterate over multiple stages
Remove the object ID and sequence number
Notes: For a write completion, the switch iterates over the stages and removes the object ID and the sequence number

## Slide 12: How to build a strongly consistent replicated system with near-linear scalability?
How to maintain the dirty set in network?
How to achieve near-linear scalability?
How to guarantee consistency?
How to handle failures?
Notes: Then let's see how harmonia achieves near-linear scalability

## Slide 13: Handling write
1
Client
Storage Servers
Primary
Backup 1
Backup 2
Write
(obj_id=A)
Switch Data Plane
obj_id | seq
E | 1
B | 2
commit=0
Notes: We apply harmonia to a PB storage with 3 replicas

## Slide 14: Handling write
1
obj_id | seq
E | 1
B | 2
A | 3
Client
Storage Servers
Primary
Backup 1
Backup 2
2
Write
(obj_id=A)
Switch Data Plane
commit=0
Add the object ID into the dirty set
Forward the request to the primary
Notes: To handle write, the switch will insert one entry to the dirty set and forward it to primary.

## Slide 15: Handling write-completion
Client
Storage Servers
Primary
Backup 1
Backup 2
3
Switch Data Plane
Write
(obj_id=A)
obj_id | seq
X | 4
C | 5
A | 3
commit=0
Notes: After the write is completed and the write-completion arrives at the switch, the switch will delete the entry from dirty set and also update the last-committed point

## Slide 16: Handling write-completion
4
Client
Storage Servers
Primary
Backup 1
Backup 2
3
Switch Data Plane
Write
(obj_id=A)
obj_id | seq
X | 4
C | 5
commit=3
Delete the entry from the dirty set
Update the last-committed point
Notes: After the write is completed and the write-completion packet arrives at the switch, the switch will delete the entry from dirty set and also update the last-committed point

## Slide 17: Handling read and reply on objects in the dirty set
1
Client
Storage Servers
Primary
Backup 1
Backup 2
2
Switch Data Plane
3
4
Read
(obj_id=E)
obj_id | seq
E | 1
B | 2
commit=0
Send the request to the Primary for consistency
Notes: To handle reads with pending writes. For example, Object E is already in the dirty set
the request will be sent to the primary for guaranteeing consistency

## Slide 18: Handling read and reply on objects not in the dirty set
1
Client
Storage Servers
Primary
Backup 1
Backup 2
2
Switch Data Plane
3
4
Read
(obj_id=C)
obj_id | seq
E | 1
B | 2
commit=0
Send the request to a Backup for better performance
Notes: When the object is not in the dirty set, for example, object C, it will be sent to a backup server for better performance

## Slide 19: How to build a strongly consistent replicated system with near-linear scalability?
How to maintain the dirty set in network?
How to achieve near-linear scalability?
How to guarantee consistency?
How to handle failures?
Sequence number + last-committed point
Notes: ideally, the dirty set is enough to guarantee consistency. But in a real, asynchronous network, the message
might have been delayed so long that a new write to the same object has been partially processed. Harmonia avoids this using the
sequence number and last-committed point which can provide enough information for the recipient
to compute if processing the read locally is safe

## Slide 20: How to build a strongly consistent replicated system with near-linear scalability?
How to maintain the dirty set in network?
How to achieve near-linear scalability?
How to guarantee consistency?
How to handle failures?
Sequence number + last-committed point
Monotonically increasing switch ID
Notes: Failure handling is critical to replicated systems.
Harmonia handles server failures based on the replication protocol.
To handle switch failures, Harmonia augments the seqnum with the switch unique ID, which is monotonically increasing when assigned to switches.
You can check out our paper for more details

## Slide 21: Implementation
Testbed
  Twelve server machines connected by a 6.5 Tbps Barefoot Tofino switch
Switch
  Written in P4
  3-stage register array for dirty set
Server
  DPDK client to generate workload
Notes: We implemented harmonia in a testbed consisting of 12 servers
on the server-side, we have custom DPDK client to generate workload

## Slide 22: Evaluation
Generality
Scalability
Comparison with in-switch storages (NetCache, NetChain)
Switch resource usage and overhead
Performance under failures
Notes: We evaluate Harmonia with respect to generality, scalability and other expierments

## Slide 23: Evaluation
Generality
Scalability
Comparison with in-switch storage (NetCache, NetChain)
Switch resource usage and overhead
Performance under failures
Notes: In this talk, we only talk about the first two.

## Slide 24: Generality with storage architectures and workloads
A general approach for
different storage architectures
A general approach for
different workloads
Notes: in this figure, we use chain replication as the baseline and compare it with applying harmonia to it.
it demonstrates that harmonia is a general...
including Redis, MongoDB and mysql.
The right figure shows it's also a general approach ...
And the performance improvement depends on R/W ratio of the benchmarks.
For example, Voter is a write-only benchmark, so harmonia has no benefit

## Slide 25: Generality with replication protocols
Primary-backup
Quorum-based
A general approach to a variety of protocols
Notes: We also show that Harmonia is a general approach to a variety of replication protocols.
These two figures show the read throughput as a function of write rate for different protocols.
The left figure shows the results for PB and CR.
Harmonia makes use of all three replicas to handle reads, and provides significantly higher throughput.
as shown by the green curve, CRAQ adds an additional phase to write so its write throughput is much lower.
We have similar results for two quorum-based protocols in the right figure

## Slide 26: Scalability
Read-only
5% Writes
Write-only
Near-linear scalability for read-intensive workloads
Notes: in the scalablity results, For CR, increasing the number of replicas does not change the overall throughput, because it only uses the tail to handle reads.
In contrast, Harmonia is able to utilize the other replicas to serve reads.
So it scales near linearly with read-intensive workloads

## Slide 27: Conclusion
Harmonia is a new replicated storage architecture
  Near-linear scalability
  Strong consistency
In-network conflict detection
  New-generation programmable switches
Notes: To conclude, Harmonia is a new replicated storage architecture
That achieves near-linear
It realizes them by the in-network...
which is implemented on the new-generataion programmable switches

## Slide 28
Thanks!
Notes: That’s all and thanks for listening